Ultrasonic Flaw Detector  bsm360

★Automatic calibration, automatic gain, dynamics repeat,

10 corridors, dormant

★DAC, AVG, B scans flaw detection tool available

★Ultra low noise, fast response, excellent performance

★quick button design for convenient operation

★Al-Mg alloy hull, super strong, waterproof dust, excellentperformance against electromagnetic interference

■Performance Features

- Measurement displaying mode: type A displaying mode, type B displaying mode;

- It is provided with linear reject function, the highest reject is 80% of the screen height;

- switch over arbitrarily among three detecting modes: single-probe , dual-probe ones and through transmission;

- It has gate setting and alarming function. Can set the position and width of gate freely on the screen, and can set alarm for forbidden wave and loss wave respectively;

- 10 detecting channels are available with a separate detecting parameter and DAC curve in every channel.

- Two input methods, angles and K value.

- Auto-gain

- Automatic generation of DAC curve by standard test block, 30 points can be recorded at most, three adjustable bias curves are generated with the function of Correction.

- Automatic generation of AVG curve by three type of flaw

- Manual B scanning

- Make test videos and Auto playback

- Users can upgrade all built-in software on PC;

- Auto shutdown,can save power ;

- It is provided with memory function, 30 A scanned images, parameters and DAC curves can be stored in every channel (10 channels in all); 30 groups of thickness values can be stored in every channel with 100 thickness values in every group;

- Can playback the saved images, call out the saved A-scan images from the memory area and display them on the screen;

- Equipped with delete function, with which any data can be deleted from storage zone;

- Two measuring unit: mm/inch;

- Real-time clock;

- Auto-calibration of probe.

- Memory of peaks.

- Can freeze and defreeze waveform and detection parameters;

- Can lock/unlock the system parameters;

- Measuring of sound path and analyze of echo times;

- Can indicate power state in real time;

- RS232 communication port available;

- Function of printing, print the report on thickness and wave amplitude curve through a serial printer;

- Can be communicated with PC, uploading the measuring data and system configuration parameters to PC    for further processing (e.g. to generate report on detection, printing, etc.);

- Having buzzer prompt during operation;

- Compact, light and easy to operate.

■ Technical Parameters

| Designation | Technical Data |
| --- | --- |
| Range of scanning (mm) | Range of scanning (mm)：0～10000 Steps: 2.5,5,10,20, 30,40,50,60,70,80,90, 100,150,200, 250, 300, 350, 400, 450,500,600,700,800,900,1000,2000,3000,4000,5000,6000,7000,8000,10000 Adjusting step: 0.1mm（2.5 mm～99.9mm），1mm（100mm～5000mm） |
| D-delay ((s) | D-delay ((s)：-20～+3400 Steps: -20,-10,0.0, 10, 20, 50,100,150,200,250,300,350,400,450,500, 600, 700,800,900,1000,1500,2000,2500,3000,3400. Adjusting steps: 0.1（-20(s～999.9(s），1（1000(s～3400(s） |
| P-delay ((s) | P-delay：0.0～99.99 Adjusting steps: 0.01 |
| MTLVEL（m/s） | MTLVEL：1000～9999 7 fixed levels: 2260,2730,3080,3230,4700,5920,6300 Adjusting steps: 1 |
| Working mode | Single probe (receiving and sending), double probe (one for receiving and another for sending), transmission (transmission probe) |
| Frequency of repeating transmitting (MHz) | 0.4–20 |
| Gain adjustment (dB) | 0～110 Adjusting step: 0.0，0.2，0.5，1，2，6，12 |
| Suppress | 0%～80% of screen height, step: 1% |
| Vertical linear error | Vertical linear error is not more than 3% |
| Horizontal linear error | Not more than 0.2% in the scanning range |
| Allowance of detection sensitivity | ≥62 dB |
| Dynamic range | ≥32 dB |
| Alarm | Three modes, i.e. forbidden wave, loss wave and auto |
| Monitoring door | 2, expressed by bold transverse line, whose start, width and height are adjustable. Adjusting range of start (mm): horizontal pixel 0~208, the displayed value is relative with the scanning range. Step: value in mm corresponding to a pixel (relative with the scanning range) Adjusting range of width (mm): horizontal pixel 4～212, the displayed value is relative with the scanning range. Step: value in mm corresponding to a pixel (relative with the scanning range) Adjusting range of height: 2%~90% of vertical graduation Step graduation: 1% |
| Display | Display: high-brightness graphic lattice |
| A-Scan display area | Full screen or local A-Scan display freezing and de-freezing A-Scan filling |
| Waveform displaying way | full wave |
| Detection channel | 10 |
| Data save | 300 A-Scan images (including setting of instrument) 30000 values of thickness (300 sets) |
| Standard communication interface with PC | RS232 |
| Measuring unit | mm/inch |
| Battery | Li battery 4×3.6V 4000mAh |
| Power adaptor | Input 100V～240V/50Hz～60Hz Output 9V～12VDC/3A～4A |
| Working temperature | 0℃～40℃ |
| Working humidity | 20%～90% |
| Port type | BNC |
| Overall dimension (mm) | 240×173×50 |
| Weight (kg) | 1.8 |